## Slide 1
HS&E INCIDENT BULLETIN |  | 2nd Quarter 2012 | 
Type of Incident | Laceration |  | 
Summary: | 
Employee was de-burring an end piece of a shroud recently cut to size from a chop saw using a vertical belt sander. During the operation the shroud caught the belt and was pulled behind the rest, pulling the shroud in the operators hand. Employee received a severe laceration causing tendon damage. | 
Root Causes: | Actions Taken Thus Far: Next Steps
Education/Training on proper use of belt sander and de-burring operation. The belt sander rest was not seated properly. Lack of cut resistant gloves while handling sharp material. Improper tool for job. De-burring machine was next to belt sander. | Retraining on safe use of power tools, grinders and PPE. Preventative maintenance intervals corrected. Improper tool removed from job. Glove policy and board reviewed and reissued.