## Slide 1
HS&E INCIDENT BULLETIN |  | 2nd Quarter 2013 | 
Location: United States | Type of incident (Struck by, puncture wound) |  | 
Summary: | No Photo available. |  |  | 
Operator was using a die grinder powered wire brush to prep a piece of stainless for weld when a piece of wire broke free then striking, penetrating weld jacket and embedding into forearm of employee. Metal wire required surgical removal. |  |  |  | 
Root Causes: | Actions Taken Thus Far: Next Steps |  |  | 
Inadequate tool for the job, low cost high bulk material not designed for heavy manufacturing thus causing premature wear of tool, training, hazard recognition, |  | Eliminate the use of wire brush if possible and find an alternative such as scotch bright pads. Review the process to purchase or limit the need for using wire brushes, review PPE requirements, JHA's, identify and additional risks/potential hazards and mitigate |  |