## Slide 1
HS&E INCIDENT BULLETIN |  | 2nd Quarter 2012 | 
Type of Incident: | Fall / Fracture |  | 
Summary: | NO PHOTO | 
Gerry Rathbun and his work partner were working on an oil hose assembly for use in a test setup. They were using a thread on style of hose fitting that require a wrench and a lot of torque to assemble. Gerry had the hose in the vice in his work area and was installing the fitting with a 36” pipe wrench when the wrench slipped off the hex fitting causing Gerry to lose his balance and fall to the floor. In the fall Gerry fractured his thumb between the first and second knuckle. |  | 
Root Causes: | Actions Taken Thus Far: Next Steps | 
The wrench used was not the best choice for this process and was worn excessively. The vice used was worn and damaged. This style of fitting is not the current industry standard. (There is now a safer, faster and easier alternative, see photos.) | Replaced the worn pipe wrench and did a department wide check of pipe wrenches for excessive ware. Replaced worn and damaged vice, also identified another in a similar condition and replaced that as well. Purchased new fittings and leased hydraulic tooling to install the current industry standard fittings. Purchased hose assemblies from a local vendor to cover test needs while waiting for new equipment and the vendor safety training that came with it. |