## Slide 1
HS&E INCIDENT BULLETIN |  | 2nd Quarter 2012 | 
Type of Incident: | Laceration |  | 
Summary: |  | 
On the VTN vertical lathe, the IP was about to go down inside the machined carter in order to check a dimension when he slips. His elbow hurt the inside diameter of the carter (cutting edge) |  | 
Root Causes: | Actions Taken Thus Far: Next Steps | 
People -Improper use of tool, equipment or material Procedures -Incomplete procedure/instructions Equipment -Inadequate or improper PPE (proper PPE not available) | Benchmark Olean for good practice on dimension checking inside machined carters Find a measurement device to check dimensions inside the carters without going down inside Find adapted arm protection (PPE) |